## Slide 1
AUTONOMOUS PRODUCTION CHOKE CONTROLLER
Problem Statement ID - Honeywell Hackathon, Problem 3A
Problem Statement Title - Autonomous Production Choke Controller for a Single Naturally Flowing Oil Well
Theme - Industrial Process Control / Oil & Gas Automation
PS Category - Software
Student Name - Divyansh Gupta (VIT Vellore)

## Slide 2: PROCESS UNDERSTANDING & MODEL
Step test: 120 hr open-loop, choke 30->40->55->45->65 %, Ts = 1 hr
Response is first-order (time constant ~5 hr on oil rate), mild noise
Opening choke RAISES oil rate but LOWERS WHP / FLP / BHP
  => the binding safety constraints are LOWER pressure bounds
Model assumptions: first-order + linear; single naturally flowing well
  (no gas lift/ESP, constant reservoir & GOR); envelope limits documented
Model: ARX(1) per output by least squares
  y[k+1] = a.y[k] + (1-a)(b0 + b1.u[k]); free-run fit 1.5-2.4 % of span
Identified steady-state gains (per % choke):
  Q +1.82 bbl/hr WHP -1.59 FLP -0.99 BHP -8.38 psi

## Slide 3: CONTROL STRATEGY
Simplified MPC by brute-force candidate search (per brief)
Each hour, enumerate choke +/- up to 5 % (ramp-feasible, fine grid)
Predict each candidate's pressures over a settling horizon + steady state
REJECT any move predicted to breach WHP/FLP/BHP + safety margin
Among safe moves, minimise (Q_ss - target)^2 + lambda.(delta choke)^2
Infeasible target => same cost settles at the highest safe rate
Monotonic first-order response: steady-state feasibility proves the
  whole trajectory safe -> safe-by-construction, 0 violations

## Slide 4: RESULTS - TARGET TRACKING (A & B)
Scenario A - Startup -> 130 bbl/hr
  settles 129.9 bbl/hr, steady-state error -0.11, 0 violations
Scenario B - Target step 100 -> 150 bbl/hr
  settles 149.7 bbl/hr, steady-state error -0.34, 0 violations
Pressures stay inside the envelope throughout
Choke moves are smooth and respect the +/-5 %/step ramp limit

## Slide 5: SAFETY PERFORMANCE & LESSONS LEARNED
Scenario C - infeasible 185 bbl/hr: controller REFUSES,
  settles at max safe 154.9 bbl/hr with 0 violations
Robust: 0 violations under +/-20% plant mismatch, unmeasured
  disturbances and 2x noise (22-case stress study, robustness.py)
Lessons learned:
  Binding constraint is a lower pressure bound, not an upper rate cap
  Monotonicity makes a cheap brute-force MPC provably safe
  Model error costs production, never safety - margin is the dial
0
MPC violations (A/B/C)
168
naive-baseline breaches on C

## Slide 6: ARTIFACTS & REFERENCES
Code (flat Python modules at repo root):
  dataio, model_id, envelope, simulator, controller, plotting, scenarios, main
Executed Jupyter notebook + technical report.md + results/ (plots, metrics.json)
Live dashboard: streamlit run app.py (scenario presets, per-step
  MPC diagnostics: candidates rejected as unsafe, WHP margin)
Robustness: python robustness.py (22 stress cases: noise, +/-20%
  mismatch, unmeasured disturbances)
Run: pip install -r requirements.txt && python main.py
  main.py asserts 0 envelope violations across A/B/C
Simulator stand-in shares the official .step(choke)->(Q,WHP,FLP,BHP)
  signature -> the real event simulator drops in with a one-line change
Repo: github.com/Divyansh2602/autonomous-choke-controller
References: least-squares system identification (Ljung); simplified
  MPC by brute-force candidate evaluation (Honeywell brief)
Required 6-trend plot (Scenario C shown)